## Slide 1
Gaussian Plume Dispersion Model
Physical Equations & Coefficients
CitySim · pollutant.cpp

## Slide 2
1 · Coordinate Rotation into Wind Frame
Meteorological convention: φ is the direction FROM which the wind blows
Wind unit vector components (world frame)
Emittor → receptor vector components
Downwind distance [m]
Crosswind offset [m]
If x ≤ 0 → receptor is upwind → C = 0. Otherwise x = max(x, x_min)
North
↑ y-world
→ x-world
↗ downwind (x∥)

## Slide 3
2 · Wind Speed — Logarithmic Profile
u_ref
Climate wind speed at reference height
h_ref
Reference height (default 10 m)
z₀
Aerodynamic roughness length (m)
u_min
Minimum wind speed floor (default 0.5 m/s)
z_e
Emittor elevation (m)
Δz_plume
User-prescribed plume rise (m)

## Slide 4
3 · Pasquill Stability Class (AUTO mode)
Determined from global horizontal irradiance I_gh and wind speed u
Condition
u < 2 m/s
2 ≤ u < 3
3 ≤ u < 5
u ≥ 5
I_gh > 600 W/m² (strong sun)
A
B
C
D
300 < I_gh ≤ 600 (moderate sun)
B
C
D
D
10 < I_gh ≤ 300 (weak sun)
C
D
D
D
I_gh ≤ 10, cloud > 0.5 (overcast)
D
D
D
D
I_gh ≤ 10, cloud ≤ 0.5 (clear night)
F
E
D
D
A = very unstable B = unstable C = slightly unstable D = neutral E = slightly stable F = stable

## Slide 5
4 · Pasquill–Gifford Dispersion Coefficients σ_y, σ_z
x = downwind distance (m) f_y, f_z = optional user scaling factors
Class
σ_y (m)
σ_z (m)
A
0.22 x (1 + 0.0001x)^{-1/2}
0.20 x
B
0.16 x (1 + 0.0001x)^{-1/2}
0.12 x
C
0.11 x (1 + 0.0001x)^{-1/2}
0.08 x (1 + 0.0002x)^{-1/2}
D
0.08 x (1 + 0.0001x)^{-1/2}
0.06 x (1 + 0.0015x)^{-1/2}
E
0.06 x (1 + 0.0001x)^{-1/2}
0.03 x (1 + 0.0003x)^{-1}
F
0.04 x (1 + 0.0001x)^{-1/2}
0.016 x (1 + 0.0003x)^{-1}

## Slide 6
5 · Gaussian Plume Concentration
Vertical term T_z — with ground reflection (image source at –H):
Q
Emission rate [kg/s]
u
Wind speed at effective height [m/s]
H
Effective stack height [m]
z
Receptor height [m]
σ_y
Lateral spread [m]
σ_z
Vertical spread [m]
y
Crosswind offset [m]
x
Downwind distance [m]

## Slide 7
6 · Optional Exponential Attenuations
Chemical / radioactive decay (first-order, rate λ [1/s])
Travel time τ = x/u converts the spatial coordinate to time for first-order kinetics.
Dry deposition (velocity v_d [m/s], mixing height h_m [m])
Models vertically-uniform removal within the mixing layer (box approximation).
Total concentration at receptor (sum over all emittors)

## Slide 8
7 · Model Assumptions & Limitations
Steady-state
No time-of-flight: emissions are assumed to have reached steady state at each hour.
Homogeneous wind
Speed and direction are uniform across the entire domain at each time step.
Flat terrain
No topography, buildings, or obstacles deflect or shelter the plume.
Perfect ground reflection
Image source at –H enforces zero vertical flux at z = 0 (no absorption).
Prescribed plume rise
ΔH is user-entered; Briggs' momentum / buoyancy rise is not computed.
Averaged wind speed for σ
Stability class uses the mean wind speed across all emittors.
P-G coefficients
Generic open-terrain Pasquill–Gifford values; not the Polish regulatory set.